## Slide 1: Simplified Telemetry Framework for the Freescale Cup
Daniel C. Castro, Matt Douthwaite, Sanket Kamthe

## Slide 2: Outline
Introduction
Bluetooth Communication
Additional Sensors
  RPM
  Ambient Light
Deliverables and Conclusion

## Slide 3: Introduction
Freescale Cup: autonomous racing car competition
Advanced teams develop custom technological solutions
Majority relies on trial and error
We propose an accessible wireless framework to acquire real-time feedback from multiple sensors.

## Slide 4: Bluetooth Communication

## Slide 5: Bluetooth Technology
Invented by Ericsson as an wireless alternative to the RS-232 protocol
Short range, low power radio communication
Widely used, over 3.5 Billion devices shipped in 2015
Bluetooth derives many properties from RS-232/serial protocol
  8-bit buffered data stream
  Asynchronous serial communication
HC-05 is a well-known and cost-effective Bluetooth module
1 cm

## Slide 6: Asynchronous Communication
Data is transmitted as a continuous stream of bytes
Byte alignment is crucial!
3F
EB
D7
DA
03
37
7A
FD
A3
Packet structure to ensure proper alignment

## Slide 7: Transmitting Simulink Blocks
Pack Bytes block
  In: stream of 64-bit double precision real-valued data
  Out: stream of 8x 8-bit vectors
Bluetooth Transmit block
  Sends these bytes at the chosen Baud rate

## Slide 8: Receiving Simulink Blocks
PC Bluetooth Receive block
  Pairs (first time) and connects to the HC-05
  Align byte stream into packet structure
  Convert back into real-valued stream

## Slide 9: Additional Sensors

## Slide 10: Measuring RPM
The two DC motors are not precisely controlled and operate independently
Accurate rotational speed data is important for closed-loop control
RPM sensor required to be:
  Contactless
  Robust against noise
  Easy to implement

## Slide 11: RPM Sensors
Infrared Sensor
  Detects a reflective surface
  Advantage:
    Will not affect rotation
  Disadvantage:
    Requires more external circuitry
    Sensitive to noise
Hall Effect Sensor
  Detects a magnetic field
  Advantages:
    Digital output robust to noise
    Widely used solution
  Disadvantage:
    Might interfere with rotation

## Slide 12: Hall Effect Implementation
Vout (V)
Time
3.3
0
Time
RPM

## Slide 13: RPM Simulink Block
Readings initially too noisy
Designed a filtering algorithm to smooth results
Exponential window: fast response to sudden changes
sampling time: noise, time resolution
triggers (magnets): quantization
window size
t-1
t-2
t
t-n
…
t
c
w
n: window size
c: count
w: weights ()
m: number of triggers
t: sampling time

## Slide 14: Measuring Ambient Light
Varying light conditions around the track interfere with the camera
Enables robust, adaptive line tracking
Analogue photodiode sensitive to visible light

## Slide 15: Deliverables and Conclusion

## Slide 16: Deliverables
Hardware guidelines
  To physically set up and connect Bluetooth module and sensors
Bluetooth Simulink blocks
Sensors Simulink blocks
Simulink
MATLAB
C++
Hardware
Implementation stack

## Slide 17: Example setup
Freedom Board (Car)
PC

## Slide 18: Conclusion
We provide:
  A simplified end-to-end telemetry framework
  Two additional sensors not originally available on the Freedom Board
Our contribution for Freescale Cup competitors:
  Enable real-time data collection for performance analysis
  Help them develop smarter closed-loop control for their cars
Possible future developments:
  Bidirectional communication for tuning the controller on the fly
  Improve physical access to hardware ports

## Slide 19: Thank you!
Questions?